COMP270 – Vector Revision
Answer the following questions on 2D vectors using pen(cil) and (graph) paper.
Pro tip: show your working – diagrams can be helpful!
1. State whether the following assertions are true or false (and if false, explain why):
  1. The vector from (1, 2) to (3, 5) is the same as the vector from (99, -100) to (101, -97).
  2. The vector from (-1, -2) to (-3, -5) is the same as the vector from (-99, -100) to (-101, -97).
  3. The size of a vector in a diagram doesn’t matter; we just need to draw it in the right place.
  4. The displacement expressed by a vector can be visualised as a sequence of axially aligned displacements.
  5. These axially aligned displacements must occur in a specific order.
  6. The vector gives the displacement from the point (x, y) to the origin.
2. Let a = and b = . Draw the following:
a	e. a + b
b	f. a - b
2a	g. a + 2b
-b	h. -2a - b

1. Evaluate the following expressions:
  1. 2
2. Write the end points of the following vectors (relative to the origin) in row format:
  1. a + b, where a = and b = describe displacements from the origin.
  2. a – b, where a = and b = describe displacements from the point (-1, -1).
  3. The vector with length 5, starting at (1, 2) and with direction pointing towards (7, 10).
3. Find the angles between the following pairs of vectors a and b using trigonometry/`SOHCAHTOA’:
  1. a = and b =
  2. a = and b =
4. For each pair of vectors in question 5, evaluate their dot product using the algebraic definition
a∙b = axbx + ayby
and check the result against your answers to question 5 using the identity
a∙b =
1. Write down any two vectors that are (i) parallel and (ii) perpendicular to:
Verify that your answers are correct using the dot product.
1. An NPC is standing at location p with a forward direction of v.
  1. How can the dot product be used to determine whether the point x is in front of or behind the NPC?
  2. Let p = and v = . For each of the following points x, determine whether x is in front of or behind the NPC:
    1. x =
    2. x =
    3. x =
    4. x =
    5. x =
    6. x =
    7. x =
2. Extending the concept from question 8, consider the case where the NPC has a limited field of view (FOV). If the total FOV angle is Φ, then the NPC can see to the left of the right of its forward direction by a maximum angle of Φ/2.
  1. How can the dot product be used to determine whether the point x is visible to the NPC?
  2. For each of the points x in question 8, determine whether x is visible to the NPC if its FOV is 90°.
  3. Suppose that the NPC’s viewing distance is also limited to a maximum distance of 7 units. Which points are visible to the NPC then?

Reference/Further reading:
3D Math Primer for Graphics and Game Development, Fletcher Dunn and Ian Parberry, CRC Press